During acceptance of trimming tool «AAAxxx» (equipment 05-7000279-001) inconsistency between 3D model of stamping mold provided by the Customer and equipment was revealed.

The following has been revealed:

The cutting part of existing 3D model of stamping mold, which is intended for die cutting the sprues out of a window inside a body, consist of 4 parts (front end  (position 1), back end (position 2) and two side parts (position 3 and 4)).

In the trimming tool received by us:

The cutting part of stamping mold is performed as one component.

| General view | General view |
| --- | --- |

| 3D model shows that part of stamping mold which is intended for die cutting the sprues out of a window inside a body, consist of 4 parts (image below). | An example: one of the parts of stamping mold shown in 3D model. |
| --- | --- |

| General view of stamping mold. Cutting part of stamping mold is performed as one component. | Part of stamping mold that not correspond to 3D model |
| --- | --- |

This discrepancy may not have negative consequences, manufacture of an pilot batch will allow to find out a situation finally. But such fact shows, that variances in structure of equipment have not been agreed between the Customer and the previous manufacturer of parts.

Findings:

- We suggest to make measurement of parts on 3D machine with objective of check the conformity of a product to parameters set by the Customer.

- Making a decision to change the construction documentation of equipment or bring equipment into conformity with the construction documentation will depend on results of gauging of a product and stability of work of equipment during the manufacture of an pilot batch.

Production manager							A. Astafyev

# Text boxes

1

4

3

2

1